## Slide 1: Line Following with TurboPi

## Slide 2: Road Map
Define Control Scheme
Process Data
Create, Train, and Test ML Model
Experiment with TurboPi

## Slide 3: The Control Scheme

## Slide 4: Line Following with IR Sensors
Use an array of IR sensors positioned at the front of the vehicle
Keep the line between the sensors to make the vehicle follow the line
Go straight
Sensor Triggered
Turn Right
Turn Left
Left Triggered
Right Triggered
No Trigger

## Slide 5: Line Following with Camera and ML
Use a camera mounted at the front of the vehicle to observe the road
Crop two sub-images from useful locations in the original image
Use classification on the sub-images to identify if the line has crossed into either image
Go straight
Sensor Triggered
Turn Right
Turn Left
Left Triggered
Right Triggered
No Trigger

## Slide 6: Data Processing

## Slide 7: Collecting Data - Opening the Files
Navigate to the Thonny IDE
  Select the Raspberry Icon in the top-left corner
  Hover over Programming
  Select Thonny
When you open Thonny, enter the password: ml4hst2023

## Slide 8: Opening the Files
To open files
  Click on File in the top left
  Select Open

## Slide 9: Collecting Data - Opening the Files
1. Go to home/turbopi/Line_Follower/
2. Double click on uwyo_data_collection.py

## Slide 10: Collecting Data

## Slide 11: Collecting Data - Compression
Open the “File Manager”
Navigate to /home/turbopi/Line_Follower/datasets
Right click the “line_following” folder
Select “Compress” from the dropdown

## Slide 12: Collecting Data - Compression
Navigate to /home/turbopi/Line_Follower/
Select “zip” as the archive type in the bottom left corner
Click “Create” when finished

## Slide 13: Transfer Data
Navigate to /home/turbopi/Line_Follower
Left click on line_following.zip to select it
Use the key combo “ctrl + c” to copy the file to your clipboard

## Slide 14: Transfer Data
On your windows computer open “File Explorer”
Navigate to Desktop/1 – TurboPi – Line Following/Data/
Use the key combo “ctrl + v” to paste the dataset into the folder

## Slide 15: Transfer Data
Right click on the transferred zip file to open a dropdown menu
Select “Extract All…” from the dropdown menu

## Slide 16: Transfer Data
One the Extract Compressed (Zipped) Folders window left click the right end of the folder path and delete “line_following”
Click “Extract” to start the extraction process

## Slide 17: Crop Data
Open the jupyter notebook “uwyo_crop.ipynb” and run the first 3 cells

## Slide 18: Label Data
Open two “File Explorer” windows
Open “File Explorer”
Right click on “Desktop” from the left hand menu bar
Select “Open in new window” from the dropdown menu

## Slide 19: Label Data
In one “File Explorer” window, open the “Data/crop” folder we created earlier
In the other “File Explorer” window, open the “Data/positive” folder

## Slide 20: Label Data
Select cropped images with black lines by holding “ctrl” with one hand and left clicking the mouse with the other hand
We will be labeling these images as positive and we are doing them first because there will be fewer of them in our dataset
Once you have all of the visible positive examples selected left click on the last image and drag it to the positive folder
Continue this process until there are no positive examples in the crop folder

## Slide 21: Label Data
Once all of your positive images have been labeled, change the positive window to the /Data/negative folder.
Use the key combo “ctrl + a” to select all of the files in the crop folder
Left click and drag to move all negative images to their respective folder

## Slide 22: Distribute Data
In the jupyter notebook “uwyo_crop.ipynb” run cell 4

## Slide 23: Machine Learning

## Slide 24: ML Considerations
The computational power of the raspberry pi is limited but decisions need to be made quickly
Things which will improve performance of the TurboPi
Reducing the size and number of cropped images
Using grayscale images (1 channel input) to reduce the computations, compared to color images (3 channel inputs)
Making the neural network as small as possible to reduce computations
Running the camera, ML, and decision process on separate threads

## Slide 25: Building an ML Model
Open the jupyter notebook “uwyoimage_trainer.ipynb”

## Slide 26: Building an ML Model

## Slide 27: Building an ML Model

## Slide 28: Experimenting with TurboPi

## Slide 29: Transfer Model to TurboPi
On your windows computer open “File Explorer”
Navigate to Desktop/1 – TurboPi – Line Following/
Use the key combo “ctrl + c” to copy line_follower.pt

## Slide 30: Transfer Model to TurboPi
On your TurboPi open “File Manager”
Navigate to /home/turbopi/Line_Follower/
Use the key combo “ctrl + v” to paste line_follower.pt

## Slide 31: Line Following - Opening the Files
Navigate to the Thonny IDE
  Select the Raspberry Icon in the top-left corner
  Hover over Programming
  Select Thonny
When you open Thonny, enter the password: ml4hst2023

## Slide 32: Line Following - Opening the Files
To open files
  Click on File in the top left
  Select Open

## Slide 33: Line Following - Opening the Files
1. Go to home/turbopi/Line_Follower/
2. Double click on uwyo_line_follower.py